## Slide 1: Embedded Programming
Amizzuddin Amin

## Slide 2: Table of Content
Reference
RECAP – Digital Output / Input
RECAP – Analog Output / Input
Digital / Analog pins available on Arduino
UART communication
Electronics equipment
Programming skill
  Ternary operator
  Object Oriented Programming (OOP)
Exercises

## Slide 3: Reference
Thinkercad account (Link)
Getting started with Arduino ebook (Link)
C programming for Arduino ebook (Link)
Arduino Reference website (Link)
C++ reference (Link)
Amizzuddin’s github (Link)
  For later part of the module (day 3 and 4)
  Purpose to enhance your programming language skill
Arduino cheat sheet (Link)
Arduino pin mapping (Link)
Return to Table of Content

## Slide 4: Recap - Digital Output/Input
Step up:
  Initialize pin => Set the pinMode(pin, mode);
    pin refers to the selected Arduino pin number
    mode refers to digital pin mode [INPUT, INPUT_PULLUP or OUTPUT]
      INPUT_PULLUP is used when no resistor is connected with the input pin. However, do note that different microcontroller have different pullup resistor values (Link)
  Digital Output [ pinMode(pin, OUTPUT) ] => digitalWrite(pin, value);
    pin refers to the selected Arduino pin to write the output value
    value refers the digital value to write to the pin [HIGH or LOW]
      HIGH = 5v and LOW = GND/ 0v
  Digital Input [ pinMode(pin, INPUT) ] => digitalRead(pin);
    pin refers to the selected Arduino pin to read the input value
      Input value can either be HIGH (voltage > 3.0v) or LOW (voltage < 1.5v) (Link)
Return to Table of Content

## Slide 5: Example
INPUT
//INPUT_PIN= Arduino pin 2
#define INPUT_PIN 2
void setup(){
pinMode(INPUT_PIN, INPUT);
}
void loop(){
bool read_input = digitalRead(INPUT_PIN);
}
OUTPUT
//OUTPUT_PIN= Arduino pin 13
#define OUTPUT_PIN 13
void setup(){
pinMode(OUTPUT_PIN, OUTPUT);
}
void loop(){
digitalWrite(OUTPUT_PIN, HIGH);
delay(500); //do nothing for 500msec
digitalWrite(OUTPUT_PIN, LOW);
delay(500); //do nothing for 500msec
}
Return to Table of Content
Program reads input from Arduino pin 2 and store the read value into variable label read_input which only stores value of HIGH or LOW(bool data_type)
Program write blink LED on Arduino board (label as “L”) every 500msec (50% duty cycle)

## Slide 6: Switch Debounce
Return to Table of Content
Problems arises when you intend to do a counter that counts up every time button is pressed. Due to the noise, microcontroller detects multiple pressed when in actual, the button is pressed once.
To solve these, one can do the following:
  By Software
  By Hardware
You can read more here how this is done
The moment button is pressed
Microcontroller detects multiple series of ONs and OFFs

## Slide 7: Recap - Analog Output/Input
Step up:
  Initialize pin => Set the pinMode(pin, mode);
    pin refers to the selected Arduino pin number
    mode refers to digital pin mode [INPUT, INPUT_PULLUP or OUTPUT]
      INPUT_PULLUP is used when no resistor is connected with the input pin. However, do note that different microcontroller have different pullup resistor values (Link)
  Analog Output [ pinMode(pin, OUTPUT) ] => analogWrite(pin, value);
    pin refers to the selected Arduino pin to write the output value
    value refers the digital value to write to the pin [0 to 255] (Link)
      PWM Duty cycle formula= (value/255) * 100% (PWM)
  Analog Input [ pinMode(pin, INPUT) ] => analogRead(pin);
    pin refers to the selected Arduino pin to read the input value
      Input value range from 0 to 1023(Link)
Return to Table of Content

## Slide 8: Example
INPUT
//POTENTIOMETER = Arduino pin A0
#define POTENTIOMETER A0
void setup(){
pinMode(POTENTIOMETER, INPUT);
}
void loop(){
int analog_value = analogRead(POTENTIOMETER);
}
OUTPUT
//OUTPUT_PIN = Arduino pin 9
#define LED_PIN 9
#define MAX_BRIGHTNESS 255
void setup(){
pinMode(LED_PIN, OUTPUT);
}
void loop(){
for(int brightness = 0; brightness < MAX_BRIGHTNESS; brightness++){
analogWrite(LED_PIN, brightness);
delay(500); //do nothing for 500msec
}
}
Return to Table of Content
Program reads potentiometer connected to Arduino pin A0 and store the read value into variable label analog_value with possible values of 0 - 1023(Link)
Program write LED on pin 9 shine brighter for every 500msec. After 128 seconds later the LED will turn off and the brightness cycle will continue.

## Slide 9: Digital / Analog pins available on Arduino
Legend:
analogWrite(pin, value);
analogRead(pin);
digitalWrite(pin, value);
digitalRead(pin);
Return to Table of Content

## Slide 10: UART communication
Step up:
  Initialize communication => Serial.begin(Baudrate);
    Baudrate refers speed of communication between devices(Link)
  Check incoming data availability => Serial.availability();
    Function returns the number of byte that is available in the serial_buffer(Link)
  Read data => Serial.read();
    Function reads a byte of data in the serial buffer. Data received is in ASCII code. (Link)
  Transmit data => Serial.print(); / Serial.write();
    Serial.print() prints data to the serial port in ASCII text. (Link)
    Serial.write() writes binary data to the serial port (Link)
Return to Table of Content

## Slide 11: Parsing receiving data
One of the challenges with UART communication is to determine how useful the data to the application.
Example: When a series of incoming data received in the serial port, How one make these data into usable command?
The solve this, both device must establish a standard protocol of communication.
Example:Transmit device can add separator marker to indicate value representation. GPS uses this type of separator as well (Link)
The next slide will provide a simple way to parse data from UART communication
Return to Table of Content

## Slide 12: Parsing receiving data
Transmit Device
Transmitter must know the type of data/commands that the receiver requires.
If receiver requires more than one data/command, data can be separated using separator marker (‘ , ‘)
Receiving Device
Receiver must be able to process data quick enough to prevent loss of data due to slow processing upon receiving data from transmitter. This is very important especially for sensitive data such as aircraft airspeed, altitude and more.
Receiver must know when reject data when data is invalid.
Sample function can be download here
Return to Table of Content

## Slide 13: Flowchart of serial_data_control() function
Return to Table of Content
Data received in Serial buffer
Read one char
Is char numeric?
Convert to decimal and store
store value = 0
Is char alphabet?
Read buffer but don’t store
Is char ‘,’ or no more data in buffer?
Is char ‘,’ or no more data in buffer?
Return the store value
Any store value?

## Slide 14: Electronics instrument
Oscilloscope
  Reads the signal from Arduino pin
  Plots the waveform from Arduino pin
Multimeter
  Read resistance, voltage or current
    Power supply NOT connected
    Measure voltage = measuring probe connected parallel to component intend to measure
    Power supply connected
    Measure voltage = measuring probe connected parallel to component intend to measure
    Measure current = measuring probe connected series to component intend to measure
Function generator
  Supplies signal such as sinewave, sawtooth wave, squarewave and triangle wave. (Commonly use for radio circuits)
Power supply
  Supplies voltage or current at the desired value
Return to Table of Content

## Slide 15: Programming Skill – Ternary Operator
If… Else.. statement
//OUTPUT_PIN = Arduino pin 9
#define LED_PIN 9
#define MAX_BRIGHTNESS 255
int brightness = 0;
void setup(){
pinMode(LED_PIN, OUTPUT);
}
void loop(){
if(brightness < MAX_BRIGHTNESS){
brightness = brightness + 1;
}
else{
brightness = 0;
}
analogWrite(LED_PIN, brightness);
delay(500); //do nothing for 500msec
}
Ternary operator
//OUTPUT_PIN = Arduino pin 9
#define LED_PIN 9
#define MAX_BRIGHTNESS 255
int brightness = 0;
void setup(){
pinMode(LED_PIN, OUTPUT);
}
void loop(){
brightness = (brightness < MAX_BRIGHTNESS) ? brightness + 1 : 0;
analogWrite(LED_PIN, brightness);
delay(500); //do nothing for 500msec
}
Return to Table of Content

## Slide 16: Programming Skill – Ternary Operator
Both of the program behaves the same way. Its just the way of writing the code.
Unlike if… else.. Statement, ternary operator is suitable for dealing value assignment for single variable. However, if you have variables need to change values at a given condition, its better to use if… else.. Statement for readability.
For more information on ternary operator you may visit the following link.
Ternary operator can be use on other programming language but the syntax may not look different. Example ternary operator on python is done this way:
Brightness = ( brightness + 1, 0) [brightness < MAX_BRIGHTNESS]
Return to Table of Content

## Slide 17: Programming Skill – Object Oriented Programming (OOP)
It is a programming model that organizes program as object.
Object is defined as data with a certain unique attributes and behaviour.
  Example:
    Object “employee” can have the following attributes:
      Division
      Department
      Designation
The benefits of OOP includes the following:
  Reusability
  Efficiency
  scalability
Return to Table of Content

## Slide 18: Programming Skill – Object Oriented Programming (OOP)
It is a programming model that organizes program as object.
Object is defined as data with a certain unique attributes and behaviour.
  Example:
    Object “employee” can have the following attributes:
      Division
      Department
      Designation
The benefits of OOP includes the following:
  Reusability
  Efficiency
  scalability
Return to Table of Content

## Slide 19: Visualizing a class in C++
Class (employee)
Access Specifier (employee salary)
Members function
(department and devision)
Data members (Name and designation)
Constructor (parameters)
Return to Table of Content

## Slide 20: Example: Pushbutton Class
Class (Pushbutton)
Private members
- counter_value;
- Debounce_duration;
- toggle_value;
- lastDebounce;
- buttonState;
Constructor
(Pin number)
Public members
- initialize()
- read()
- change_of_state()
- toggle()
- clickers()
Return to Table of Content

## Slide 21: L293N Truth table
Decimal | INA | INB | INC | IND | Motor direction | EN
0 | 0 | 0 | 0 | 0 | Stop | The enable input is used to control the speed of motor. To control speed of motor can be done using PWM (analogWrite(pin, value)) function.
1 | 0 | 0 | 0 | 1 | Radial turn | 
2 | 0 | 0 | 1 | 0 | Radial turn | 
3 | 0 | 0 | 1 | 1 | Stop | 
4 | 0 | 1 | 0 | 0 | Anti-clockwise | 
5 | 0 | 1 | 0 | 1 | Forward | 
6 | 0 | 1 | 1 | 0 | Spot turn | 
7 | 0 | 1 | 1 | 1 | Radial turn | 
8 | 1 | 0 | 0 | 0 | Clockwise | 
9 | 1 | 0 | 0 | 1 | Reverse | 
10 | 1 | 0 | 1 | 0 | Forward | 
11 | 1 | 0 | 1 | 1 | Radial turn | 
12 | 1 | 1 | 0 | 0 | Stop | 
13 | 1 | 1 | 0 | 1 | Radial Turn | 
14 | 1 | 1 | 1 | 0 | Radial Turn | 
15 | 1 | 1 | 1 | 1 | Stop | 
Return to Table of Content

## Slide 22: Beginner level Practice
Control LED brightness using Potentiometer.
Control 3 LED blink using pushbutton such that it replicates a traffic light.
Control motor direction using the code develop from practice 2
Control motor speed using potentiometer using the code develop from practice 1 (motor turn anti-clockwise)
Combine codes from practice 3 and 4. Are you able to control both speed and direction of motor using pushbutton and potentiometer?
Tip: you can use the map() function to make data conversion from potentiometer to control motor speed

## Slide 23: Intermediate level Practice
Control 3 LED blink using serial communication such that it replicates a traffic light.
Control LED brightness using serial communication
Control the motor direction and speed using serial communication.
Tip: You can use this function to simplify your development for serial communication.

## Slide 24: Advance level Practice
Control multiple servo to replicate Robotic arm via serial communication.
Display string on LCD display via serial communication.
Tip: You may use this function to simplify your serial communication development.

## Slide 25: Practice Solution
Basic
  Link
  Link
  Link
  Link
  Link (with class Link)
Intermediate
  Link
  Link
  Link
Advance
  Link
  Link
Extra
  Dual motor control (pushbutton and potentiometer) – using class
  Parsing serial communication (accept only numeric values)